## Slide 1
GRADUATION PROJECT DEFENSE
Open-Source SOC Pipeline
Engineering an End-to-End Threat Detection, Orchestration, and Case Management Lab Under Real Hardware Constraints
Wazuh
Shuffle
TheHive
Sysmon
MITRE ATT&CK
AlienVault OTX
OPEN-SOURCE SOC PIPELINE
01
Notes: Open with a strong hook: this is a real, operational SOC, not a diagram exercise. State the one-sentence thesis: an end-to-end open-source detection, orchestration, and case-management pipeline engineered under a strict 16GB laptop budget. Introduce yourself and the course context briefly, then move to the problem. Timing: 30-45s. Likely question: why build this instead of using a cloud SOC trial. Answer: the goal was to understand and engineer every integration point by hand, including the failure modes.

## Slide 2
THE PROBLEM
Why This Project Exists
Modern SOC stacks (SIEM + SOAR + Threat Intel + Case Management) are built for enterprise hardware — not a single laptop.
Goal: a functional, automated threat detection, orchestration, and case-management lab that runs reliably within strict hardware limits.
Constraint: a single 16 GB RAM host laptop, without severely degrading its physical SSD through constant virtual-machine swapping.
Standard reference tools (Splunk, MISP, Cortex) assume RAM and storage budgets this environment simply does not have.
THE CONSTRAINT
16 GB
Total host RAM — shared with the hypervisor, browser, and OS
38-50 GB
Thin-provisioned disk shared across SIEM + SOAR + Case Mgmt indices
OPEN-SOURCE SOC PIPELINE
02
Notes: Explain that enterprise SOC reference architectures assume dedicated servers, not a single laptop shared with the hypervisor and browser. Emphasize the RAM math: 16GB total, minus what the host OS and VMware need, leaves very little for two VMs plus 6+ services. Common question: why not just use a cloud lab or free-tier SaaS SIEM? Answer: the objective was hands-on engineering of the full stack, including its constraints, not consuming a managed product.

## Slide 3
GOALS
Objectives & Key Requirements
Decoupled, Event-Driven Pipeline
Telemetry streams to the SIEM; alerts pass through a validation loop, trigger the SOAR for enrichment, then push to Case Management.
MITRE ATT&CK Mapping
Every custom detection rule must map to a specific ATT&CK technique — not just raise a generic alert.
Dynamic SLA Enforcement
Alert severity must automatically apply the correct Time-to-Acknowledge / Contain / Resolve targets.
Cloud Threat Intelligence
Use cloud-based IOC enrichment APIs instead of a locally hosted database, to preserve host memory.
OPEN-SOURCE SOC PIPELINE
03
Notes: Walk through the four requirements as design constraints, not just a wish list, each one forced a specific architectural choice discussed later. Point out that MITRE mapping and SLA enforcement are what separate this from a toy lab. Likely question: how did you decide on SLA time windows? Answer: based on industry-standard SOC SLA tiers, scaled to the technique's real-world urgency, e.g. credential dumping is Critical with a 15-minute acknowledge target.

## Slide 4
THE APPROACH
Proposed Solution
Build the entire stack from mature, open-source tooling — no commercial licensing, full control over configuration.
Adopt a hybrid deployment: Wazuh installed natively for stability, remaining services (Shuffle, TheHive, Cassandra) containerized for portability.
Replace heavyweight local components (MISP) with lightweight cloud threat-intelligence APIs to respect the memory budget.
Engineer custom detection rules mapped to MITRE ATT&CK, feeding a SOAR workflow that enriches and auto-escalates through a defined SLA matrix.
SLA DETERMINATION MATRIX
Severity
TTA
TTC
TTR
Critical
15m
1h
4h
High
30m
4h
24h
Medium
2h
12h
48h
Low
8h
N/A
7d
Example: Critical = Credential Dumping (T1003.001)
OPEN-SOURCE SOC PIPELINE
04
Notes: Frame this as the blueprint slide: open-source only, hybrid deployment, cloud threat intel, and a rule-to-SLA pipeline. Point at the SLA matrix and note that severity is not arbitrary, it is tied directly to attacker technique. Likely question: what happens when nothing hits a rule? Answer: no alert is generated, this is precision detection, not blanket logging; future work adds detection-gap validation to catch that failure mode.

## Slide 5
ARCHITECTURE
System Architecture
SOC-Backend — Ubuntu Server VM
8 GB RAM · 2 vCPU · 40-50 GB thin-provisioned disk
Static IP 192.168.196.132 (Netplan, ens33)
Native Wazuh (systemd) — SIEM engine
Dockerized: Shuffle, TheHive, Cassandra, OpenSearch on soc-network bridge
Endpoint-Victim — Windows 10/11 VM
4 GB RAM · 2 vCPU · 50 GB thin-provisioned disk
DHCP IP 192.168.196.133
Sysmon telemetry generation (SwiftOnSecurity config)
Target for Atomic Red Team adversary emulation
Wazuh Agent → Manager
Decoupled event-driven design: the host laptop runs both VMs side-by-side; the Ubuntu backend hosts the entire SOC stack while the Windows VM exists purely to generate realistic attacker telemetry.
OPEN-SOURCE SOC PIPELINE
05
Notes: This is the core architecture diagram, spend real time here. Point to each VM and its resource allocation, then trace the arrow: Sysmon on Windows forwards to the Wazuh Agent, which reports to the Wazuh Manager on the Ubuntu backend. Mention static IP addressing keeps the lab reproducible. Likely question: why split RAM 8GB/4GB instead of evenly? Answer: the backend runs six services simultaneously and needs the larger share; the endpoint only needs to run Sysmon and occasional Atomic Red Team scripts.

## Slide 6
DEPLOYMENT
Environment
Hypervisor: VMware Workstation, chosen for stable dual-VM virtualization on a single laptop.
Hybrid deployment model: Wazuh installed natively on Ubuntu (managed via systemd) after Docker-based Wazuh proved unreliable.
Remaining SOC services — Shuffle, TheHive, Cassandra, OpenSearch — run as Docker containers on a custom soc-network bridge.
SSD-protection measures: mainMem.useNamedFile = FALSE in the .vmx file, and vm.swappiness = 1 on the Ubuntu guest.
WHY HYBRID?
Native Wazuh
Stable — avoids the SSL/hostname bugs baked into Wazuh's Docker images
Dockerized services
Shuffle / TheHive / Cassandra isolated, portable, individually resource-capped
Thin provisioning
Prevents VMware from instantly claiming 100+ GB of physical SSD space
OPEN-SOURCE SOC PIPELINE
06
Notes: Explain the hybrid deployment as a lesson learned, not the original plan: Wazuh was originally meant to be containerized like everything else, but SSL certificate issues forced a native install. Mention the two SSD-protection settings, useNamedFile=FALSE and swappiness=1, as deliberate hardware-preservation engineering. Likely question: doesn't running Wazuh natively break your all-Docker consistency? Answer: yes, and that's an explicit tradeoff, documented as a design decision on a later slide, stability outweighed consistency here.

## Slide 7
TOOLING
Technology Stack
Layer | Technology | Role
Hypervisor | VMware Workstation | Dual-VM virtualization on one host
SIEM | Wazuh 4.7.2 | Log ingestion, decoding, rule matching
SOAR | Shuffle (latest ghcr.io) | Webhook orchestration, JSON transform, API calls
Case Management | TheHive 5.2 (:9000) | Incident workflow & alert tracking
Databases | OpenSearch 2.11.0 · Cassandra 4.0 | Backend for Wazuh/Shuffle · Backend for TheHive
Telemetry | Sysmon (SwiftOnSecurity config) | Granular process, file, network events
Threat Intel | AlienVault OTX · VirusTotal · AbuseIPDB | Cloud IOC enrichment via Shuffle
Adversary Emulation | Atomic Red Team | Safe, mapped ATT&CK technique execution
Dropped: MISP (2-4 GB RAM footprint) and Cortex — both removed to respect the 16 GB host budget; replaced by free cloud API nodes in Shuffle.
OPEN-SOURCE SOC PIPELINE
07
Notes: Move through the table quickly, this is reference material, not the story. Spend the most time on the 'Dropped' callout: MISP and Cortex were in the original plan but were cut for RAM reasons. Likely question: what would you gain back by adding MISP later? Answer: a private, queryable IOC history rather than depending entirely on external API rate limits, worth revisiting once hardware allows.

## Slide 8
PIPELINE
End-to-End Data Flow
Windows
Endpoint
Sysmon
Wazuh
Python
Integration
Shuffle
AlienVault
OTX
TheHive
Telemetry from the Windows endpoint is captured by Sysmon and forwarded via the Wazuh Agent to the Manager.
Level-12 critical alerts trigger a Python integration script that posts JSON to Shuffle's webhook listener.
Shuffle sanitizes the payload, enriches indicators via AlienVault OTX, then issues a direct HTTP POST to TheHive to raise an Alert.
OPEN-SOURCE SOC PIPELINE
08
Notes: Trace this diagram left to right as the literal path one alert takes. Emphasize the Python Integration step, this is where Wazuh hands off to the SOAR, and it's a custom script, not an out-of-the-box connector. Likely question: what happens if Shuffle is down when Wazuh tries to send an alert? Answer: the Python script has an exponential backoff retry loop, three attempts with increasing delay, before giving up.

## Slide 9
DETECTIONS
Detection Engineering
Detections are engineered from Sigma-style logic, then hand-mapped to Wazuh custom XML rules — every rule carries an explicit MITRE ATT&CK tag.
All custom rules are elevated to Level 12 (“Critical”) so they trigger the Wazuh → Shuffle integration automatically.
MITRE Technique | Wazuh Rule | Detection Logic
T1033 — System Owner/User Discovery | 100005 (Lvl 12) | whoami execution via sysmon_event1
T1003.001 — OS Credential Dumping: LSASS | 100010 / 100011 | lsass.exe access · comsvcs.dll MiniDump
T1003.002 — SAM Credential Dump | 100015 | reg save on the SAM hive
T1087.001 — Local Account Discovery | 100016 | net(1)?.exe user ¦ localgroup
OPEN-SOURCE SOC PIPELINE
09
Notes: This is the technical core professors will probe hardest. Walk through one rule end-to-end, e.g. T1003.001 LSASS access: explain the Sigma-style logic behind rule 100010 and why it's mapped to Level 12. Likely question: why two separate rules (100010, 100011) for the same technique? Answer: they catch two distinct attack surfaces for the same technique, direct LSASS process access versus the comsvcs.dll MiniDump living-off-the-land method, both needed for coverage.

## Slide 10
SOAR
Automation Workflow — Shuffle
Webhook
Port 5001 — receives Wazuh Level-12 alert JSON
Regex Node
Replaces \ with / in Windows paths to prevent JSON-escape crashes
AlienVault OTX
GET ipv4 search — enriches extracted indicators
HTTP POST
Sends a hand-built, clean JSON payload directly to TheHive's API
THEHIVE ALERT PAYLOAD (KEY FIELDS)
Title ← $exec.rule.description | Source ← “Wazuh” | SourceRef ← $exec.id
Summary ← agent name/IP, sanitized command line, and the OTX enrichment result
Severity (1-4), TLP/PAP flags, and Tags: ["Sysmon", "Wazuh", "Enriched", "CRITICAL_INCIDENT"]
OPEN-SOURCE SOC PIPELINE
10
Notes: Explain the Regex node first since it's the least obvious but most critical piece, without it, Windows file paths crash the JSON parser downstream. Then walk the enrichment step and the final POST to TheHive. Likely question: why not let TheHive's own Shuffle connector do this? Answer: covered in the Engineering Challenges slide, the graphical connector had a placeholder bug that broke JSON parsing; the raw HTTP node was a deliberate workaround.

## Slide 11
TROUBLESHOOTING
Engineering Challenges
Storage Exhaustion
Problem: 38 GB disk filled; OpenSearch threw cluster_block_exception, freezing TheHive & Shuffle. Fix: Pruned Docker images/logs, unlocked the read-only index block, planned disk expansion.
JSON Escaping Crash
Problem: Windows paths (C:\\Users\\...) broke Shuffle's JSON parser on \\W / \\z sequences. Fix: json.dumps() in the Python webhook + a Shuffle Regex node converting \\ to /.
TheHive Connector Bug
Problem: Shuffle's graphical TheHive app sent unquoted ${flag} placeholders, crashing JSON parsing. Fix: Replaced the app node with a raw HTTP POST carrying a clean, hardcoded payload.
Wazuh Docker SSL Mismatch
Problem: Containerized Wazuh threw x509 hostname errors (demo.indexer vs wazuh.indexer). Fix: Abandoned Dockerized Wazuh; moved to a native systemd installation.
OPEN-SOURCE SOC PIPELINE
11
Notes: These four issues are the heart of the engineering story, don't rush this slide. For each: state the symptom exactly as it appeared in logs, the root cause, and the fix, in that order, it shows systematic debugging rather than guesswork. Likely question: which of these took the longest to resolve? Answer: be honest based on your own experience, likely the JSON escaping issue or the Wazuh SSL mismatch, since both required tracing the failure across two different systems.

## Slide 12
REASONING
Design Decisions — and Why
Native Wazuh, not Docker
The Docker image's SSL certs are hardcoded for the wrong hostname. Native install (systemd) removed that entire failure class.
Docker for the rest of the stack
Shuffle, TheHive, and Cassandra gain resource isolation and portability without the certificate baggage Wazuh's image carried.
HTTP node instead of TheHive connector
The graphical connector injected unquoted placeholders. A hand-built HTTP POST guarantees valid JSON every time.
Cloud threat intel over local MISP
MISP alone needs 2-4 GB RAM. AlienVault OTX delivers the same enrichment over a free API call.
Thin provisioning everywhere
Keeps VMware from instantly claiming 100+ GB of physical SSD, preserving disk headroom on a constrained laptop.
OPEN-SOURCE SOC PIPELINE
12
Notes: This slide answers the 'why' behind every choice on the previous slides, treat it as the reasoning summary. Emphasize that each decision was a direct response to a concrete failure, not a preference. Likely question: if you had more RAM available, would you make the same choices? Answer: probably keep the HTTP node and cloud threat intel regardless, since they're more reliable, but might reconsider MISP and containerized Wazuh once certificate issues are resolved upstream.

## Slide 13
LIVE RESULTS
Demonstration Results
Detection
Wazuh matches custom rules; whoami & Atomic Red Team executions elevate to Level 12 critical.
OPERATIONAL
Enrichment
Shuffle sanitizes the command line and queries AlienVault OTX for the extracted indicator.
OPERATIONAL
Alert Creation
A clean JSON payload is POSTed directly to TheHive's REST API — no connector failures.
OPERATIONAL
Case Management
TheHive generates an Alert with MITRE tags and indicators, ready for analyst triage.
OPERATIONAL
OPEN-SOURCE SOC PIPELINE
13
Notes: If a live demo is possible, this is the slide to transition into it: trigger whoami or an Atomic Red Team technique on the Windows VM, then show the alert landing in TheHive in real time. If demoing live isn't possible, walk through screenshots in this exact order: Wazuh alert, Shuffle execution log, TheHive alert. Likely question: how long does the full pipeline take end-to-end? Answer: near real-time, typically a few seconds from Sysmon event to TheHive alert, since there's no batching in the pipeline.

## Slide 14
HONEST ASSESSMENT
Technical Debt & Limitations
HIGH
Storage Exhaustion Risk
50 GB remains tight. Continuous log ingestion will eventually require expanding the disk to 60-80 GB and resizing the partition.
DEBT
Fragile TheHive Integration
The hardcoded HTTP POST bypasses TheHive's connector UI — any future API schema change breaks ticket creation silently.
DEBT
Security Posture Limitation
plugins.security.disabled=true on OpenSearch enables Shuffle connectivity but is unacceptable outside an isolated lab.
MEDIUM
Memory Swap Wear
swappiness=1 mitigates SSD wear, but sudden traffic spikes still hit the 4-6 GB Linux swap file, causing I/O pressure.
OPEN-SOURCE SOC PIPELINE
14
Notes: This slide demonstrates engineering maturity, showing you know the limitations of your own system is a strength, not a weakness. Be direct about the OpenSearch security-plugin-disabled decision, it's the one a security-minded examiner will flag immediately, so get ahead of it. Likely question: isn't disabling OpenSearch security a serious vulnerability? Answer: yes, explicitly acknowledged, it is only acceptable because this is an isolated, air-gapped lab network with no external exposure; it would be unacceptable in any production deployment.

## Slide 15
ROADMAP
Future Work
1
PHASE 1
Scale Adversary
Emulation
Execute remaining ART techniques: Credential Dumping (T1003.001) & Event Log Clearing (T1070.004).
2
PHASE 2
Scale Detection
Rules
Add Wazuh rules for Sysmon Event ID 10 (LSASS targeting) and Event ID 1 (wevtutil.exe cl).
3
PHASE 3
Dynamic SLA
Routing
Shuffle Multi-Path Split node to assign severity by rule ID and map accurate SLA timers.
4
PHASE 4
Continuous
Validation
Weekly Invoke-AtomicTest cron jobs; flag a Detection Gap if Wazuh misses a 5-minute window.
5
PHASE 5
Metrics
Dashboard
Report MTTD, MTTR per severity tier, and False Positive Rate (FPR).
OPEN-SOURCE SOC PIPELINE
15
Notes: Frame this as a realistic next-phase plan, not vague aspiration, each phase has a concrete deliverable. Highlight Phase 4, continuous validation, as the most valuable next step since it turns the lab from a one-time demo into an ongoing detection-quality feedback loop. Likely question: which phase would you tackle first? Answer: likely Phase 2, scaling detection rules, since it directly increases MITRE coverage with the least new infrastructure risk.

## Slide 16
SUMMARY
Conclusion
A fully operational, open-source SOC pipeline — engineered end-to-end within a strict 16 GB hardware budget.
Detection → enrichment → case management runs automatically, end to end.
Real engineering tradeoffs — storage limits, JSON parsing, SSL certs, connector bugs — solved, not avoided.
Every custom rule maps to MITRE ATT&CK, with an SLA matrix driving response priority.
OPEN-SOURCE SOC PIPELINE
16
Notes: Close by tying back to the opening thesis: a hardware-constrained laptop now runs a genuinely functional SOC pipeline. Reiterate that the value of the project is in the engineering decisions and the debugging, not just the final green checkmarks. Keep this brief, 30-45 seconds, and transition directly into questions.